## Slide 1
Spanning tree
protocol Implementation
110550070 郭傑誠

## Slide 2
Spanning tree protocol
  A loop in a network -> broadcast storm、 duplicate frames
  Root bridge election
  Assign ports role
  STP deal with route failure
switch 1
switch 2
switch 3

## Slide 3
Root bridge election
Select the switch with lowest id as root
switch 1
switch 2
switch 3
Send Hello BPDU to each other
(Bridge protocol data unit)
root bridge
6
1
2

## Slide 4
Assign port role
  Set all root bridge ports to designated port
2. Other switches choose a port be root port (least cost)
3. Ports connected to root port set to designated port
4. Remained port is blocked port

## Slide 5
switch 1
switch 2
switch 3
root bridge
6
1
2
designated port
designated port
designated port
root port
root port
blocked port

## Slide 6
STP deal with route failure
  Max age timer: Expired when no hello BPDU was received
2. Change port state, role if needed.

## Slide 7
switch 1
switch 2
switch 3
root bridge
6
1
2
designated port
designated port
designated port
root port
root port
blocked port

## Slide 8
switch 1
switch 2
switch 3
root bridge
6
1
designated port
root port
root port
root port

## Slide 9
switch 1
switch 2
switch 3
root bridge
6
1
designated port
root port
designated port
root port

## Slide 10
Thank you for listening!